## Slide 1
HA230、HA280 AND DNA230 IN HEMOPERFUSION

## Slide 2
1
2
Background of Poisoning
Principle and benefits of HA230
3
Clinical studies
4
Operation of HA230
5
Introduction of HA280 and DNA230
Notes: My introduction will be divided into foour parts: the background of poisoning, Principle of HA230, and some clinical studies of HA230 application in different poisoning. and operation of HA230

## Slide 3
1
2
Review and Validation of potential papers / Case reports from other countries important for us eg Turkey etc.. All member, (John, schenider Thomas ,olivier)
Hemoperfusion in terms of protocols vs different specialities ( Surgical / Trauma(john prowle) / Burn (Thomas,schneider )/ Paediatric(ricci,italy) ) with HA 380 all of them.
3
Validation of our tutorials ( booklet scheneider,Olivier,– Video,ronco, ) and corrections if necessary
4
Get proposal in terms of Webinars themes like pro /Con(all of them)

## Slide 4
Background of
Poisoning
1
Notes: so lets take a look at some background of poisoning first

## Slide 5
WHO Region | Total no. suicides (World Health Organiation, 2014) | Estimated % of suicides due to pesticide poisoning in the region | Estimated no. pesticide suicides | % of each region's population contributing to the estimate
High-income countries | 192000 | 1.7 | 3300 | 89.7
African Region | 61000 | 3.5 | 2100 | 5.9
the Americas | 35000 | 8.8 | 3100 | 95.7
Eastern Mediterranean Region | 30000 | 7.1 | 2100 | 33.4
European Region | 35000 | 0.9 | 300 | 56.2
South East Asia Region | 314000 | 11.3 | 35500 | 69.1
Western Pacific Region | 131000 | 48.3 | 63300 | 92.3
Total | 798000 | 13.7 | 109700 | 
Annual estimated number and percentage of suicides in each WHO region (2010-2014)
The global burden of fatal self-poisoning with pesticides 2006-15: Systematic review
World Health Organization, 2014
POISONING OVERVIEW
1
Part
Notes: According to official statistic globally, the acute poisoning is mainly caused by pesticide, industrial toxin, drug overdose, biotoxin and others.
The global poisoning causes are similar, but the proportion of these causes of poisoning are different according to different regional conditions.
According to the table, we could found that the total amount of global pesticide death is nearly 110 thousand cases per year. Especially in Africa and South East Asia or even in Eastern Mediterranean, South America, there are many people suffering from pesticide.

## Slide 6
POISONING OVERVIEW
1
Part
Notes: According to official statistic globally, the acute poisoning is mainly caused by pesticide, industrial toxin, drug overdose, biotoxin and others.
The global poisoning causes are similar, but the proportion of these causes of poisoning are different according to different regional conditions.
According to the table, we could found that the total amount of global pesticide death is nearly 110 thousand cases per year. Especially in Africa and South East Asia or even in Eastern Mediterranean, South America, there are many people suffering from pesticide.

## Slide 7
Other fatal
complications
Cells destruction
or death
Tissue hypoxia
and ischemia
Respiratory depression
or apnea
Severe organ injuries
Pulmonary edema
Hallucinations
Renal failure
CONSEQUENCE OF POISONING
1
Part
CONSEQUENCE
Notes: Poisoning may destroy or even kill the cells and lead to tissue hypoxia or even severe organ injuries such as pulmonary edema, renal failure.
Besides, the central nervous system will be affected, patients will have hallucinations. And many other fatal complications will be induced.

## Slide 8
Factors affecting the prognosis of poisoning
1
Part
Different time to use the same treatment method
may lead to absolutely different effects.
Due to
treatment
Product 02
Due to
individuality
The toxicity of poisons
The dosage of poisons
The treatment time
Early effective measures
Transportation
Distribution
Metabolism
Excretion
Notes: So after the treatment, two factots will affect the pronosis of poisoning.
Treatment and individuality.
Treatment effectioon depends on the

## Slide 9
?
No specific antidote
Before definite diagnose
Poor efficacy
Unknown or multiple drugs mixed
Side effect
ACUTE POISONING CONTROL
1
Part
Therapeutic Principles
Stop contacting the poisons
Clean the undigested poisons in vivo
Fasten the excretion of poison
Apply specific antidotes
Related Symptomatic treatment
Weakness
Notes: The basic clinical method for poisoning are 5 as follows. We usually stop the contacting of poisons, scavenge the undigested poisons in vivo, fasten the excretion of poison, apply the specific antidotes and other related Symptomatic treatment.
Actually, there are some problems in clinical practice. For some poisons, we do not have specific antidote and make no sense of the drugs.
Before definite diagnose, we could not conduct accurate treatment. And these basic method has poor efficacy and slow effect which may worsen the patients’condition.

## Slide 10
1
3
4
Hemodialysis
（HD）
（HF）
Hemofiltration
Hemoperfusion （HP）
Plasma Exchange （PE）
Small water soluble substance
Methanol,
ethylene glycol,
lithium
2
Water soluble substance
Small molecules
Part of medium molecules
Hydrophobic
Middle to large molecules
All kind of toxin in blood
Disadvantage:
Dose effect relationship
Infection
BLOOD PURIFICATION
1
Part
Notes: So is there any other way to treat poisoning?
There are some Blood purification methods commonly used in clinical practice such as HD, HF,PE,HP are common used for poisoned.
PE could directly remove the toxins from the blood but has its disadvantages such as high risk of infection.
HP is designed to remove hydrophobic substances.
And hydrophobicity is the typical characteristic of the most poisons.

## Slide 11
2
Principle and benefits of
HA230
Notes: SO how does our HA230 work?

## Slide 12
Hydrophobicity
Molecular Sieve
Physical adsorption/Van der Waals
Electrostatic interaction
HA230 Hemoperfusion Cartridge
2
Part
Notes: This is the HA230 hemoperfusion cartridge. Inside the cartridge are the resin showed as brown bead. And under the Electron Microscope we can see the inner surface of the resin with the 3D network structure works as the molecule sieve.
Based on the principle of hydrophibility and interactions, when the blood goes through, it only the specific toxins will be adsorbed.
So that is the mechanism of HA230.

## Slide 14
Morphine
Cocaine
Dopamine
Pentobarbital
Diazepam
Tetramine
Drugs with organic ring in the molecular structure are easily adsorbed.
benzene ring
Hydrophobic Structure
2
Part
Notes: Especially, drugs with organic ring in the molecular structure are easily adsorbed. Such as Morphine with benzene ring.

## Slide 16
Digoxin
Cytostatics
HA230 Indications
2
Part
Notes: Based on the principle we talked above, HA230 hemoperfusion cartridge can be used for poisoning caused by pesticide, Biotoxin, drug overdose...etc
For example, in India, Snake bite is the most common indication ，and In Germany, a new indication has been developed, using HA230 for cancer patients to remove excessive cytostatics to relieve complications of chemotherapy.

## Slide 17
Comparison of Charcoal & Resin
2
Part
Materials | Charcoal | Resin
Adsorbents | Activated charcoal | Neutral macro-porous resin
Mesh size | Unselective | 13~15nm (selective)
Property | None-selectivity | Relative specificity
Aim substance | Small to middle molecules | Middle to macro molecules Protein-bound molecules
Security | 1.Harmful to blood cells 2.Poor bio-compatibility 3.Weak skeleton: easily break off and form embolism | 1.Smooth surface 2.Good bio-compatibility 3.Strong skeleton
Application | Widely use in poisoning | Poisoning, immune disease, liver disease, renal failure…
Notes: lets compara another adsorbent charcoal with resin.

## Slide 18
Safety: Lab monocyte test
Static Test
Dynamic Test
Results
No evidence of increased necrosis or apoptosis in monocytes exposed to the cartridges both in the static and dynamic tests.
HA cartridges carry an level of biocompatibility and their use in HP is not associated with adverse reactions or signs of cytotoxicity.

## Slide 19
Results
Sequential images demonstrated an excellent distribution of the flow inside the cartridges.
The structural and functional design of the studied cartridges is adequate for hemoperfusion without channeling phenomena.
Safety: Radiological results

## Slide 20
3
Clinical studies
Notes: Let me show you some clinical studies of HA230 application.

## Slide 21: HA230 for Paraquat
Notes: This is a multicenter retrospective study for paraquat posoning treatment.

## Slide 22
HA230 for Paraquat - Conclusion
Notes: Apart from that, they found that the 60 day survival post HP+CVVH and HP was largely improved than the conservative group. So they comes to the result that …

## Slide 23
ASOP= Acute severe organophosphate poisoning
Repeated HP Group: n=20 received 3-4 times HP within 48 hrs;
Single HP Group: n=16 received once HP
HA230 for ASOP
3.2
Part
Notes: Another publication is on the comparison of once HP treatment and repeated HP treatment for acute severe organophosphate poisoning on 1st day. They enrolled 36 patients and divided them into 2 groups. For group 1 with 20 patients who received 3-4times HP within 48 hrs. For group 2 with 16 patients who received once HP treatment.
Acute Severe Organic Phosphorus Poison)

## Slide 24
IMS: intermediate myasthenia syndrome
Conclusion:
Early repeated HP is more efficient than single HP in treating acute severe organophosphate poisoning.
HA230 for ASOP – Result & Conclusion
3.2
Part
Notes: According to the result of treatment efficacies, they concluded that early hemoperfusion is more efficient than single hemoperfusion in treating organophosphate poisoning.

## Slide 25
104 patients with acute Carbamazepine poisoning
Group A (HP in Emergency Department)=51
Group B (HP in the blood purification room)=34
Group C (No HP)=19
HA230 for Carbamazepine
3.4
Part
Notes: group A, who received HP treatment in the Emergency Department; group B, who received HP treatment in the blood purification room; and group C,
who did not received HP treatment.
[,kɑrbə'mæzə,pin]

## Slide 26
Improve the consciousness recovery, survival and shorten the hospital stay day
Glasgow coma score
HA230 for Carbamazepine – Result & Conclusion
3.4
Part
Notes: Epileptic seizures
a significant difference in the state of consciousness was seen at 4 h after admission: GCS scores in group A were significantly higher than those of groups B and C (P b 0.05).

## Slide 27
Initial condition:
A young female who presented to ER with alleged history of consumption of 17.5 mg of digoxin tablets. After admission to ICU, she developed atrioventricular blocks with hemodynamic instability. 亲脂疏水？
Case Study ：HP for Suicidal Digoxin
3.5
Part
From Dr.Deven Juneja, India
Notes: And also we are collecting cases globally and tthere are alsp drug overdose cases. let me show you a case study that happened in india

## Slide 28
Conclusion: Resin hemoperfusion may be successfully and safely used as an alternative therapy, in combination with other supportive measures, to manage patients with digoxin toxicity especially when Fab fragments are unavailable.
High serum digoxin levels
Bradyarrhythmias with hypotension
Non-availability of Fab fragments of antidigoxin antibodies
HP for 4hrs
Gradual symptomatic improvement
Heart rate also improved
Atrio-ventricular block got corrected over the next 24 hrs.
Then continue to remain asymptomatic
Discharged after 4 days of hospitalization
Result
Case Study ：HP for Suicidal Digoxin
3.5
Part
From Dr.Deven Juneja, India

## Slide 29
HA230 for HDMTX
3.2
Part
HDMTX:High-dose Methotrexate
Notes: Another publication is on the comparison of once HP treatment and repeated HP treatment for acute severe organophosphate poisoning on 1st day. They enrolled 36 patients and divided them into 2 groups. For group 1 with 20 patients who received 3-4times HP within 48 hrs. For group 2 with 16 patients who received once HP treatment.
Acute Severe Organic Phosphorus Poison)

## Slide 30
HA230 for HDMTX
3.8
Part
.
Case Report: implementation of HA-230 hemoadsorption procedure to remove cumulated MTX from the body and reduce its toxicity in a child with ALL after high-dose chemotherapy
Notes: Of course, there are many other indications reported such as acute wasp stings and abrin poisoning.

## Slide 31
Acute wasp stings
Abrin poisoning
Other Publications
3.8
Part
Notes: Of course, there are many other indications reported such as acute wasp stings and abrin poisoning.

## Slide 32
Accelerate poisons elimination
Reduce metabolic substances
Alleviate complications
Keep internal environment stable
Shorten hospitalization
Improve survival
Clinical Suggestions:
As early as possible
More frequent HP treatment at beginning(1-3 times/day)
Longer treatment time
Pesticide & Herbicide
Rodenticide
Biotoxin
Drug overdose
Industrial toxin
Sum Up
3
Part
Notes: As we shared such cases of using HA230,lets usm up this part.

## Slide 33
4
Operation of HA230

## Slide 34
Compatible with All KINDS of MACHINES
CRRT
Hemodialysis
HDF
JF-800A
Notes: Easy to use

## Slide 35: Operation
Recommendations:
Treatment Time: < 6h
Blood flow rate: 100~320 ml/min
Anticoagulant:
Heparin
first-dose: 62.5~125U/kg
additional dose: 1250～2500U/h
Citrate
4% sodium citrate 100-250ml/h input from the artery, keep ACT within 200～250s.
keep free calcium within 0.20-0.40mmol/L in vitro；
1.00-1.20mmol/L in vivo.
Notes: 单独全血灌流，常规 HA230 for Poisoning is commonly conducted by directly blood hemoperfusion singly. And it can be also conducted with other treatment methods such as HD,CVVH.
The treatment time we recommend is less than 6hr. And the blood flow rate is recommended from 0-300. Commonly speaking, the flow rate is around 200ml/min. Heparin and citrate are the common anticoagulants for the poisoned patients. Any treatment parameters could be adjusted according to the actual conditions.
200ml/minjingc
In clinic, we usually set the blood flow rate around 0-300ml/min. The common anticoagulant are heparin and citrate. For heparin, the first dosage is around 62.5-125U/kg and the additional dosage is 1250U-2500U/h. This is the HA230 treatment mode. HA230 could be conducted singly on hemoperfusion machine, hemodialysis machine or single pump machine. Besides it can be combined with HD treatment, HDF treatment or CVVH treatment on related machines when patients have renal injuries. So the operation of HA230 is quite flexible and suitable for emergency cases.

## Slide 36
5
Introduction of HA280 and DNA230

## Slide 37: HA280 Disposable Hemoperfusion Cartridge
HA280 can relieve patients from autoimmune disease, specifically removes numerous immune related pathogenic factors and improves prognosis.
Common Treatment Mode of HA280：
Notes: HA280 can relieve patients from autoimmune disease such as allergic pupura rapidly and effectively, and specifically removes numerous immune related pathogenic factors and improves prognosis.

## Slide 38: DNA immunoadsorption (IA)
Immunoadsorption therapy refers to the combination of highly specific antigen or antibody or substance with specific physical and chemical affinity (ligand) with adsorbent material (carrier).
Ligand
Protein
RBC
WBC
Platelet
Targeted molecules
Carrier
Flow Direction
Notes: Immunoadsorption therapy refers to the combination of highly specific antigen or antibody or substance with specific physical and chemical affinity (ligand) with adsorbent material (carrier). When blood or plasmapasses through this adsorbent, it can specifically adsorb the corresponding pathogenic factors in the body and purify the blood.

## Slide 39: DNA230 Immunoadsorbent Column
DNA230 is especially designed for Systemic Lupus Erythematosus (SLE) and its complications based on the immunoadsorption therapy.
DNA230 can specifically adsorb ANA & anti-ds-DNA antibodies and clear pathogenic immunologic complexes, accordingly ease SLE symptom, protect kidney function, enhance drug sensitivity, reduce the side effect of medicine treatment and improve patients' prognosis.

## Slide 40
WHY JAFRON PRODUCTS
3.Improve hemodynamic; Benefit organ function;
Reduce the ICU stay; improve survival.
1. Compatible with all blood purification machines such as hemodialysis machine, CRRT machines, ECMO, CPB
2.Easy to operate and connect and safety issue approved
For more details, please log onto the website www.jafron.com to learn about more products.

## Slide 41
Scan to register
at jafronclub.com
Scan to watch webinar 2020
at jafron.com
Welcome to join us!
@Jafron Biomedical
JAFRONCLUB

## Slide 42
98, Technology Six Road, High-Tech Zone, 519085, Zhuhai, China
+86 (756) 3689 708
en.jafron.com
support@jafron.com
Contact Us:
Jafron: make every resin with best quality